Chapter 21: Input/Output Macros

The IBM System/360 and those that have followed in the family have evolved an elaborate I/O system in an attempt to maintain efficiency in processing extremely large data sets.  Even the early System/360 designs had several levels in the I/O architecture: logical IOCS (Input/Output Control System), Physical IOCS, and the Channel subsystem.  While such a multi–level organization can be very efficient, it is somewhat hard to program.

From an Assembler Language level, the proper control and use of I/O operations requires several sequences of instructions.  Many times, these sequences appear as a fixed set of instructions in a fixed order, with optional parameters.  Such sequences immediately suggest the use of macros with keyword parameters.  Indeed, this is the common practice.

To review from the previous chapter, the use of a macro is based on a macro definition that is then invoked by what is called the “macro invocation”.  As a standard example, we recall the decimal divide macro.  This first definition is that of a positional macro.

Again, we note an obvious fact.  Teaching examples tend to be short and explicit.  This sample macro is so simple that few programmers would actually use it.  However, the I/O macros that are the subject of this chapter are complex; nobody writes the equivalent code.

A MACRO begins with the key word MACRO, includes a prototype and a macro body, and ends with the trailer keyword MEND.   Parameters to a MACRO are prefixed by the ampersand “&”.  Here is the example definition.

Header				MACRO

Prototype			DIVID	&QUOT,&DIVIDEND,&DIVISOR

Model Statements		ZAP		&QOUT,&DIVIDEND
				DP		&QUOT,&DIVISOR

Trailer				MEND

The macros used in the I/O system seem all to be keyword macros.  The definition of a keyword macro differs from that of a positional macro only in the form of the prototype.  Each symbolic parameter must be of the form &PARAM=[DEFAULT].  What this says is that the symbolic parameter is followed immediately by an “=”, and is optionally followed by a default value.  As a keyword macro, the above example can be written as:

Header				MACRO

Prototype			DIVID2   &QUOT=,&DIVIDEND=,&DIVISOR=

Model Statements		ZAP      &QOUT,&DIVIDEND
				DP       &QUOT,&DIVISOR

Trailer				MEND

Here are a number of equivalent invocations of this macro, written in the keyword style.  Note that this definition has not listed any default values.

DIVID2   &QUOT=MPG,&DIVIDEND=MILES,&DIVISOR=GALS

DIVID2   &DIVIDEND=MILES,&DIVISOR=GALS,&QUOT=MPG

DIVID2   &QUOT=MPG,&DIVISOR=GALS,&DIVIDEND=MILES

It is possible to use labels defined in the body of the program as default values.

MACRO

DIVID2  &QUOT=MPG,&DIVIDEND=,&DIVISOR=

ZAP     &QOUT,&DIVIDEND
         DP      &QUOT,&DIVISOR

MEND

With this definition, the two invocations are exactly equivalent.

DIVID   MPG,MILES,GALS
         DIVID2  &DIVIDEND=MILES,&DIVISOR=GALS

The invocation of the macro DIVID2 will expand as follows:

ZAP     MPG,MILES
         DP      MPG,GALS

Having reviewed the syntax of keyword macros, we now turn to the main topic of this chapter: a brief discussion of the Input/Output Control System and associated macros.  Following the lead of Peter Abel [R_02], the focus will be on the following:

DCB	Data Control Block, used to define files.

OPEN	This makes a file available to a program, for either input or output.

CLOSE	This terminates access to a file in an orderly way.  For a buffered output
			approach, this ensures that all data have been output properly.

GET	This makes a record available for processing.

PUT	This writes a record to an output file.  In a buffered output, this may
			write only to an output buffer for later writing to the file.

Register Usage

Each I/O macro that we shall discuss expands into a sequence of calls to operating system routines, most probably in the LIOCS (Logical I/O Control System) level.  For this reason, we should review the general–purpose registers used by the operating system.

0 and 1	Logical IOCS macros, supervisor macros, and other IBM 
			macros use these registers to pass addresses.

13		Used by logical IOCS and other supervisory routines to hold the 
			address of a save area.  This area holds the contents of the user 
			program’s general purpose registers and restores them on return.

14 and 15	Logical IOCS uses these registers for linkage.  A GET or PUT
			will load the address of the following instruction into register 14 
			and will load the address of the actual I/O routine into register 15.

This use of registers 13, 14, and 15 follows the IBM standard for 
			subroutine linkage, which will be discussed in a later chapter.

One “take away” from this discussion is the fact that user programs should reference and use only registers 3 through 12 of the general–purpose register set.  Some general–purpose registers are less “general purpose” than others.

Record Blocking

In IBM terminology, a data set is a collection of data records that can be made available for processing.  The term is almost synonymous with the modern idea of a disk file; for most of this text the two terms will be viewed as equivalent.  One should realize that the idea of a data set is more general than that of a disk file.  Data sets can be found on a DASD (Direct Access Storage Device, either a magnetic disk or a magnetic drum), on magnetic tape, or on a sequence of paper punch cards.  The term “data set” is a logical construct.

In order to understand the standard forms of record organization, one must recall that magnetic tape was often used to store data.  This storage method had been introduced in the 1950’s as a replacement for large boxes of punched paper cards.  The standard magnetic tape was 0.5 inches wide and either 1200 or 2400 feet in length.  The tape was wound on a removable reel that was about 10.5 inches in diameter.  The IBM 727 and 729 were two early models.

The IBM 727 was officially announced on September 25, 1963 and marketed until May 12, 1971.  The figure at left was taken from the IBM archives, and is used by permission.

It is important to remember that the tape drive is an electro–mechanical unit.  Specifically, the tape cannot be read unless it is moving across the read/write heads.  This implies a certain amount of inertia; physical movement can be started and stopped quickly, but not instantaneously.

One physical manifestation of this problem with inertia is the inter–record gap on the magnetic tape.  If the tape contains more than one physical record, as do almost all tapes, there must be a physical gap between the records to allow for starting and stopping the tape.  In other words, the data layout on the tape might resemble the following:

One issue faced early by the IBM design teams was the percentage of tape length that had to be devoted to these inter–record gaps.  There were several possible solutions, and each one was pursued.  Better mechanical control of the tape drive has always been a good choice.

Another way to handle this problem would be to write only large physical records.  Larger records lead to a smaller percentage of tape length devoted to the inter–record gaps.  The efficiency problem arises with multiple small records, such as images of 80–column cards.

One way to improve the efficiency of storage for small records on a magnetic tape is to group the records into larger physical records and store these on tape.  The following example is based on the one above, except that each physical record now holds four records.  Note the reduction of the fraction of tape length devoted to inter–record gaps.

This process of making more efficient use of tape storage is called record blocking.  The program reads or writes logical records that have meaning within the context of that program.  These logical records are blocked into physical records for efficiency of storage.  In a particular data set, all physical records will contain the same number of logical records; the blocking factor is a constant.  The only exception is the last physical record, which may be only partially filled.

Consider a set of 17 logical records written to a tape with a blocking factor of 5.  There would be four physical records on the tape.
	Physical record 1 would contain logical records 1 – 5,
	physical record 2 would contain logical records 6 – 10,
	physical record 3 would contain logical records 11 – 15, and
	physical record 4 would contain logical records 16 and 17.

On a physical tape, it is likely that the last physical record will be the same size as all others and be padded out with dummy records.  In the above example, physical record 4 might contain two logical records and three dummy records.  This is a likely conjecture.

Magnetic tape drives are not common in most computer systems these days, but the design feature persists into the design of the modern data set.

Use of the I/O Facilities

In order to use the data management facilities offered by the I/O system, a few steps are necessary.  The program must do the following:

1.	Describe the physical characteristics of the data to be read or written with respect to 
		data set organization, record sizes, record blocking, and buffering to be used.

2.	Logically connect the data set to the program.

3.	Access the records in the data set using the correct macros.

4.	Properly terminate access to the data set so that buffered data (if any)
		can be properly handled before the connection is broken.

While some of these steps might be handled automatically by the run–time system of a modern high–level language, each must be executed explicitly in an assembler program.

Style Conventions for Invoking I/O Macros

Some of the I/O macros, especially the file definition macro, require a number of parameters in order to specify the operation.  This gives rise to a stylistic convention designed to improve the readability of the program.  The most common convention used here is to use the keyword facility and list only one parameter per line.

While one possibly could use positional parameters in invoking an I/O macro, this would require any reader to consult a programming reference in order to understand what is intended.  Of course, it is possible for a programmer to forget the proper argument order.

Here is a file definition macro invocation written in the standard style.

FILEIN   DCB   DDNAME=FILEIN,                                          X

DSORG=PS,                                               X

DEVD=DA,                                                X

RECFM=FB,                                               X

LRECL=80,                                               X

EODAD=A90END,                                           X

MACRF=(GM)

Note the “X” in column 72 of each of the lines except the last one.  This is the continuation character indicating that the next physical line is a continuation of the logical line.  To reiterate a fact, it is the presence of a non–blank character in column 72 that makes the next line a continuation.  Peter Abel [R_02] places a “+” in that column; that is good practice.

Here is another style that would probably work.  It is based on old FORTRAN usage.

FILEIN   DCB   DDNAME=FILEIN,                                          1

DSORG=PS,                                               2

DEVD=DA,                                                3

RECFM=FB,                                               4

LRECL=80,                                               5

EODAD=A90END,                                           6

MACRF=(GM)

Note that every line except the last has a comma following the parameter.  This is due to the fact that the parameter string after the DCB should be read as a single line as follows:

DDNAME=FILEIN,DSORG=PS,DEVD=DA,RECFM=FB,LRECL=80,EODAD=A90END,MACRF=(GM)

The File Definition Macro

The DCB (Data Control Block) is the file definition macro that is most commonly used in the programs that we shall encounter.  As noted above, it is a keyword macro.  While the parameters can be passed in any order, it is good practice to adopt a standard order and use that exclusively.  Some other programmer might have to read your work.

The example above shows a DCB invocation that has been shown to work on the particular mainframe system now being used by Columbus State University.  It has the form:

Filename  DCB  DDNAME=Symbolic_Name,                                   X

DSORG=Organization,                                     X

DEVD=Device_Type,                                       X

RECFM=Format_Type,                                      X

LRECL=Record_Size,                                      X

EODAD=EOF_Address,                                      X

MACRF=(Input_Operation)

The name used as the label for the DCB is used by the other macros in order to identify the file that is being accessed.  Consider the following pair of lines.

The example macro has one problem that might lead to confusion.  Consider the line:

Filename  DCB  DDNAME=Symbolic_Name,                                   X

The file name is the same as the symbolic name.  This is just a coincidence.  In fact it is the filename, which is the label associated with the DCB, that must match the other macros.

Here is an explanation of the above entries in the invocation of the DCB macro.

DDNAME identifies the file’s symbolic name, such as SYSIN for the primary system input device and SYSPRINT for the primary listing device.  Here we use a slightly nonstandard name FILEIN, which is associated with SYSIN by a job control statement near the end of the program.  That line is as follows:

//GO.FILEIN DD *

The “*” in this statement stands for the standard input device, which is SYSIN.  This statement associates the symbolic name FILEIN with SYSIN.

DSORG identifies the data set organization.  Typical values for this are:
	PS		Physical sequential, as in a set of cards with one record per card.

DEVD defines a particular I/O unit.  The only value we shall use is DA, which indicates a direct access device, such as a disk.  All of our I/O will be disk oriented; even our print copy will be sent to disk and not actually placed on paper.

RECFM specifies the format of the records.  The two common values of the parameter are:
	F		Fixed length and unblocked
	FB		Fixed length and blocked.

LRECL specified the length (in bytes) of the logical record.  A typical value would be 
a positive decimal number.  Our programs will all assume the use of 80–column punched cards for input, so that we set LRECL=80.

BLKSIZE specifies the length (in bytes) of the physical record.  Our sample invocation does not use this parameter, which then assumes its default value. If the record format is FB (fixed length and blocked), the block size must be an even multiple of the logical record size.  If the record format is F (fixed length and unblocked), the block size must equal the logical record size.  It is probably a good idea to accept the default value for this parameter.

EODAD is a parameter that is specified only for input operations.  It specifies the symbolic address of the line of code to be executed when an end–of–file condition is encountered.

MACRF specifies the macros to be used to access the records in the data set.  In the case of GET and PUT, it also specifies whether a work area is to be used for processing the data.  The work area is a block of memory set aside by the user program and used by the program to manipulate the data.  We use MACRF=(GM) to select the work area option.

The OPEN Macro

This macro opens the data set and makes its contents available to the program.  More than one dataset can be opened with a single macro invocation.  The upper limit on datasets for a single OPEN statement is 16, but that number would produce unreadable code.  As a practical matter, your author would prefer an upper limit of two or three datasets for each invocation of the OPEN macro.

Consider the following two sequences of macro invocations.  Each sequence does the same thing; it opens two datasets.

Sequence 1 is a single statement.

OPEN (FILEIN,(INPUT),PRINTER,(OUTPUT))

Sequence 2 has two statements, which could appear in either order.

OPEN (FILEIN,(INPUT))
          OPEN (PRINTER,(OUTPUT))

Each of these statements assumes that the two Data Control Blocks are defined.

FILEIN    DCB    Define the input file here
PRINTER   DCB    Define the output file here

The general format of the OPEN macro for one file is as follows [R_21, page 67].

[LABEL]    OPEN (ADDRESS[,(OPTIONS)]

Multiple files can be opened at the same time, by continuing the argument list.

[LABEL]    OPEN (ADDRESS1[,(OPTIONS1),ADDRESS2[,(OPTIONS2)]

Note that the first argument for opening the dataset is the file name used as the label for the DCB that defines the dataset.  This is the label (address) associated with the DCB, not the symbolic name of the file (SYSIN, SYSPRINT, etc.).

It is also possible to pass the address of the DCB in a general–purpose register.  When a register is used for this purpose, it is enclosed in parentheses.  Here are two equivalent code sequences, each of which opens FILEIN for INPUT.

* OPTION 1
          OPEN (FILEIN,(INPUT))
*
* OPTION 2
          LA R2,FILEIN
          OPEN ((2),(INPUT))

Note the parentheses around the second argument in each of the two individual invocations of the OPEN macro.  This is a use of the sublist option for macro parameters [R_17, p. 302].  A sublist is a character string that consists of one or more entries separated by commas and enclosed in parentheses.  What is happening here is that the macro definition is written for a sublist as a symbolic parameter, and this is a sublist of exactly one item.

There is one advantage in creating a separate OPEN statement for each file to be opened.  If the macro fails, the line number of the failing statement will be returned.  With only one file per line, the offending file is identified immediately.

The Close Macro

This macro deactivates the connection to a dataset in an orderly fashion.  For output datasets, this will flush any data remaining in the operating system buffers to the dataset, so that nothing is lost by closing the connection.  If needed, this macro will update any catalog entries for the dataset; in the Microsoft world this would include the file attributes.

Once a dataset is closed, it may be accessed again only after it has once again been opened.

While it may be possible to execute a program and terminate the execution without issuing a CLOSE for each open file, this is considered very bad programming practice.

The general format of the CLOSE macro for one file is as follows [R_21, page 27].

[LABEL]    CLOSE (ADDRESS[,(OPTIONS)]

Multiple files can be closed at the same time, by continuing the argument list.

[LABEL]    CLOSE (ADDRESS1[,(OPTIONS1),ADDRESS2[,(OPTIONS2)]

The code that has been successfully used in our lab assignments seems not to be of 
this form.  Here are the lines that we have used to close the INPUT and PRINTER.

A90END   CLOSE FILEIN

CLOSE PRINTER

The format above is that preferred for use when running under the DOS operating system, which is an IBM product not related to the better known Microsoft product.  Our programs are run under a variant of the OS operating system.  According to the standard format for OS, the above statements should have been written as follows.

A90END   CLOSE (FILEIN)

CLOSE (PRINTER)

Apparently, either form of the CLOSE macro for a single file will work.

When closing more than one file with a single CLOSE macro, one must allow for the fact that the options do exist, even if not commonly used.  Here is the proper format.

A90END   CLOSE (FILEIN,,PRINTER)

Notice the two commas following FILEIN.  This indicates that optional parameter list 
OPTIONS1 is not used.  Were only one comma present, the assembler would try to interpret the string PRINTER as an option for closing FILEIN.  The lack of options following the string PRINTER indicates that no options are used for that close either.

Locate Mode

The next two system macros to be discussed are GET and PUT.  Before discussing either of these, it is important to note an I/O mode that will not be discussed here.  This is called “locate mode”; it allows direct processing of data in the system buffers, so that the program need not define a work area.  As this is a very minor advantage [R_02, page 262], we shall omit this feature and assume that each GET and PUT references a work area.

The GET Macro

This macro makes available the next record for processing.  The record input overwrites the previous contents of the input area.  There are two general formats as used with a work area.

[label]   GET  Filename,Workarea

[label]   GET (1),(0)

In each of these formats, the label is optional (the reason it is shown in brackets).  The filename is that used as the label for the DCB.  The system delivers the record to the work area, as specified in the second argument.

In the following examples, the file name is FILEIN and the work area is labeled RECDIN.  Here are two equivalent code sequences.  The first sequence uses the first format.

GET  FILEIN,RECDIN

FILEIN   DCB  Define the input file

RECDIN   DS   CL80     This is the input work area

The second uses the use of general–purpose registers 0 and 1 in the standard manner to store the addresses of the file definition area and the work area

LA  1,FILEIN    Address of the file definition

LA  0,RECDIN    Address of the work area

READIT   GET (1),(0)     Read a record into RECDIN.  Note the
                         standard use of the parentheses.

The PUT Macro

This macro writes a record from the output work area. There are two general formats.

[label]   PUT  Filename,Workarea

[label]   PUT (1),(0)

In each of these formats, the label is optional (the reason it is shown in brackets).  The filename is that used as the label for the DCB.  The system delivers the record to the work area, as specified in the second argument.

In the following examples, the file name is PRINTER and the work area is labeled DATOUT.  Here are two equivalent code sequences.  The first sequence uses the first format.

PUT  FILEIN,RECDIN

PRINTER   DCB  Define the input file

DATOUT    DS   CL133     This is the output work area

The second uses the use of general–purpose registers 0 and 1 in the standard manner to store the addresses of the file definition area and the work area

LA  1,PRINTER   Address of the file definition

LA  0,DATOUT    Address of the work area

PUT (1),(0)     Copy data from work area to printer.

Expansion of the I/O Macros

47          OPEN  (PRINTER,(OUTPUT))

000014                            48+         CNOP  0,4

000014 4510 C016         0001C    49+         BAL   1,*+8

000018 8F                         50+         DC    AL1(143)

000019 000098                     51+         DC    AL3(PRINTER)

00001C 0A13                       52+         SVC   19

53          OPEN  (FILEIN,(INPUT))

00001E 0700                       54+         CNOP  0,4

000020 4510 C022         00028    55+         BAL   1,*+8

000024 80                         56+         DC    AL1(128)

000025 0000F8                     57+         DC    AL3(FILEIN)

000028 0A13                       58+         SVC   19

59          PUT   PRINTER,PRHEAD

00002A 4110 C092         00098    61+         LA    1,PRINTER

00002E 4100 C1A2         001A8    62+         LA    0,PRHEAD

000032 1FFF                       63+         SLR   15,15

000034 BFF7 1031         00031    64+         ICM   15,7,49(1)

000038 05EF                       65+         BALR  14,15

66          GET   FILEIN,RECORDIN

00003A 4110 C0F2         000F8    68+         LA    1,FILEIN

00003E 4100 C152         00158    69+         LA    0,RECORDIN

000042 1FFF                       70+         SLR   15,15

000044 BFF7 1031         00031    71+         ICM   15,7,49(1)

000048 05EF                       72+         BALR  14,15

95 A90END   CLOSE (FILEIN)

000074                            96+         CNOP  0,4

000074 4510 C076         0007C    97+A90END   BAL   1,*+8

000078 80                         98+         DC    AL1(128)

000079 0000F8                     99+         DC    AL3(FILEIN)

00007C 0A14                      100+         SVC   20

101          CLOSE (PRINTER)

00007E 0700                      102+         CNOP  0,4

000080 4510 C082         00088   103+         BAL   1,*+8

000084 80                        104+         DC    AL1(128)

000085 000098                    105+         DC    AL3(PRINTER)

000088 0A14                      106+         SVC   20

116 PRINTER  DCB   DSORG=PS,

DDNAME=PRINTER,

RECFM=FM,

LRECL=133

119+*                       DATA CONTROL BLOCK

120+*

000098                     121+PRINTER  DC    0F'0'          ORIGIN ON

122+*                       DIRECT ACCESS DE

000098 0000000000000000    123+         DC    BL16'0'        FDAD, DVTB

0000A8 00000000            124+         DC    A(0)           KEYLEN, DE

125+*                       COMMON ACCESS ME

0000AC 00                  126+         DC    AL1(0)         BUFNO, NUM

0000AD 000001              127+         DC    AL3(1)         BUFCB, BUF

0000B0 0000                128+         DC    AL2(0)         BUFL, BUFF

0000B2 4000                129+         DC    BL2'0100000000000000' DSO

0000B4 00000001            130+         DC    A(1)           IOBAD FOR

131+*                       FOUNDATION EXTEN

0000B8 00                  132+         DC    BL1'00000000'  BFTEK, BFA

0000B9 000001              133+         DC    AL3(1)         EODAD (END

0000BC 82                  134+         DC    BL1'10000010'  RECFM (REC

0000BD 000000              135+         DC    AL3(0)         EXLST (EXI

136+*                       FOUNDATION BLOCK

0000C0 D7D9C9D5E3C5D940    137+         DC    CL8'PRINTER'   DDNAME

0000C8 02                  138+         DC    BL1'00000010'  OFLGS (OPE

0000C9 00                  139+         DC    BL1'00000000'  IFLGS (IOS

0000CA 0050                140+         DC    BL2'0000000001010000' MAC

141+*                       BSAM-BPAM-QSAM I

0000CC 00                  142+         DC    BL1'00000000'  OPTCD, OPT

0000CD 000001              143+         DC    AL3(1)         CHECK OR I

0000D0 00000001            144+         DC    A(1)           SYNAD, SYN

0000D4 0000                145+         DC    H'0'           INTERNAL A

0000D6 0000                146+         DC    AL2(0)         BLKSIZE, B

0000D8 00000000            147+         DC    F'0'           INTERNAL A

0000DC 00000001            148+         DC    A(1)           INTERNAL A

149+*                            QSAM INTERF

0000E0 00000001            150+         DC    A(1)           EOBAD

0000E4 00000001            151+         DC    A(1)           RECAD

0000E8 0000                152+         DC    H'0'           QSWS (FLAG

0000EA 0085                153+         DC    AL2(133)       LRECL

0000EC 00                  154+         DC    BL1'00000000'  EROPT, ERR

0000ED 000001              155+         DC    AL3(1)         CNTRL

0000F0 00000000            156+         DC    H'0,0'         RESERVED A

0000F4 00000001            157+         DC    A(1)           EOB, INTER

158 ****************************************

159 *

160 *     INPUT FILE - DATA CONTROL BLOCK

161 *

162 ****************************************

163 FILEIN   DCB   DSORG=PS,

MACRF=(GM),

DEVD=DA,

DDNAME=FILEIN,

EODAD=A90END,

RECFM=FB,

LRECL=80

166+*                     DATA CONTROL BLOCK

167+*

0000F8                     168+FILEIN   DC    0F'0'          ORIGIN ON

169+*                       DIRECT ACCESS DE

0000F8 0000000000000000    170+         DC    BL16'0'        FDAD, DVTB

000108 00000000            171+         DC    A(0)           KEYLEN, DE

172+*                       COMMON ACCESS ME

00010C 00                  173+         DC    AL1(0)         BUFNO, NUM

00010D 000001              174+         DC    AL3(1)         BUFCB, BUF

000110 0000                175+         DC    AL2(0)         BUFL, BUFF

000112 4000                176+         DC    BL2'0100000000000000' DSO

000114 00000001            177+         DC    A(1)           IOBAD FOR

178+*                       FOUNDATION EXTEN

000118 00                  179+         DC    BL1'00000000'  BFTEK, BFA

000119 000074              180+         DC    AL3(A90END)    EODAD (END

00011C 90                  181+         DC    BL1'10010000'  RECFM (REC

00011D 000000              182+         DC    AL3(0)         EXLST (EXI

183+*                       FOUNDATION BLOCK

000120 C6C9D3C5C9D54040    184+         DC    CL8'FILEIN'    DDNAME

000128 02                  185+         DC    BL1'00000010'  OFLGS (OPE

000129 00                  186+         DC    BL1'00000000'  IFLGS (IOS

00012A 5000                187+         DC    BL2'0101000000000000' MAC

188+*                       BSAM-BPAM-QSAM I

00012C 00                  189+         DC    BL1'00000000'  OPTCD, OPT

00012D 000001              190+         DC    AL3(1)         CHECK OR I

000130 00000001            191+         DC    A(1)           SYNAD, SYN

000134 0000                192+         DC    H'0'           INTERNAL A

000136 0000                193+         DC    AL2(0)         BLKSIZE, B

000138 00000000            194+         DC    F'0'           INTERNAL A

00013C 00000001            195+         DC    A(1)           INTERNAL A

196+*                            QSAM INTERF

000140 00000001            197+         DC    A(1)           EOBAD

000144 00000001            198+         DC    A(1)           RECAD

000148 0000                199+         DC    H'0'           QSWS (FLAG

00014A 0050                200+         DC    AL2(80)        LRECL

00014C 00                  201+         DC    BL1'00000000'  EROPT, ERR

00014D 000001              202+         DC    AL3(1)         CNTRL

000150 00000000            203+         DC    H'0,0'         RESERVED A

000154 00000001            204+         DC    A(1)           EOB, INTER