Two’s Complement Arithmetic

We now address the issue of representing integers as binary strings in a computer.

There are four formats that have been used in the past; only one is of interest to us.

The four formats are

1.	Sign–Magnitude

2.	One’s–Complement

3.	Two’s–Complement

4.	Excess–N, where N is some positive integer; say 127 for Excess–127.

Sign–magnitude representation is obsolete.

Excess–127 representation is only used as part of floating point representations.
		If discussed at all, it will be in the context of the IEEE–754 standard.

We focus on Two’s–complement, but discuss one’s–complement arithmetic as
	a mechanism for generating the two’s complement.

Representation of Non–Negative Integers

In each of one’s–complement and two’s–complement arithmetic, no special steps
	are required to represent a non–negative integer.

All conversions to the complement number systems begin with conversion to simple
	binary representation, often from decimal notation.

The only issue with non–negative integers is to insure that the number is not too large
	for the number of bits used in the representation.

There are two ways to define this size limitation in the complement numbers system.
	1.	The most significant bit (leftmost) must be a “0” for non–negative numbers.
	2.	For an N–bit representation, the number must be less than 2N–1.

The biggest signed 8–bit integer is	27 – 1 =	127.
The biggest signed 16–bit integer is	215 – 1 =	32767.

Three 8–bit examples:	100	=	0110 0100
	22	=	0001 0110
	0	=	0000 0000

Leading Zeroes Are Significant

When we talk about any number system that can represent signed integers, we must
	specify the number of bits used to represent the number.

Each binary representation must have that number of bits.  This means padding
	non–negative numbers with leading zeroes.

Thus, we could say	100	= 110 0100
	22	= 1 0110
	0	= 0.

But, when we discuss 8–bit numbers, we MUST SAY
	100	=	0110 0100
	22	=	0001 0110
	0	=	0000 0000

The common integer sizes for signed arithmetic are 8–bit, 16–bit, and 32–bit.

I have worked with 12–bit, 18–bit, 30–bit, and 36–bit signed integers.
These are of interest only for assigning problems to students.

Taking the One’s–Complement

To take the one’s complement of a binary integer, just
		Change every 0 to a 1
		Change every 1 to a 0

One’s–complement arithmetic is that arithmetic that uses the one’s–complement of
	a binary integer to represent its negative.

+ 100 in 8–bit	one’s complement.		0110 0100.

– 100 in 8–bit one’s complement.
		Convert 100 to 8–bit binary	0110 0100
		Take the one’s complement	1001 1011
		– 100 is represented as		1001 1011

+ 22 is 8–bit one’s complement		0001 0110

– 22 in 8–bit one’s complement
		Convert 22 to 8–bit binary	0001 0110
		Take the one’s complement	1110 1001
		– 22 is represented as		1110 1001

We no longer use one’s–complement arithmetic.  It has two serious problems.

Problems with One’s–Complement Arithmetic

There are two serious problems with the use of one’s–complement arithmetic.  The first one will be described but not explained.

Problem 1:	It is a lot trickier to build a binary adder for one’s–complement numbers.
			Just take my word for this one.

Problem 2:	Negative Zero

Consider 8–bit one’s–complement arithmetic

+ 0 is					0000 0000

Take the one’s complement	1111 1111

So – 0 is represented by		1111 1111

Most of us are uneasy about having a distinct – 0 in our number system.

Code such as the following is considered strange.
		if ( ( x == 0) || (x == –0) )

This course will not cover one’s–complement arithmetic or use it directly for any purpose other than taking the two’s complement, discussed next.

Taking the Two’s Complement

There are two processes for taking the two’s complement of a number.  The one that students find the most natural involves first taking the one’s complement and then adding 
1 to that complement.

We must then cover the addition of two binary bits, specifically mentioning each of the
sum bits and carry bits.  The analog in decimal arithmetic is to say that the sum of 5 and 5 is 0 with a carry of 1.  Yes, 5 + 5 = 10, generating two digits from 2 one–digit numbers.

Here is the binary addition table

| A | B | Sum | Carry |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 |
| 1 | 1 | 0 | 1 |

Yes, 1 + 1 is really 2.  We denote this by saying that the sum 1 + 1 carries 1
into the two’s column.

Consider 5 + 7		5 =	0101
				7 =	0111
					1100	12

Taking the Two’s Complement (Part 2)

The recipe for taking the two’s–complement of a binary number is simple.

1.	Take the one’s–complement of the number
	2.	Add 1 to that complement.

+ 100 in 8–bit two’s–complement binary		0110 0100

– 100 in 8–bit two’s–complement binary
	Represent +100 as an 8–bit number		0110 0100
	Take the one’s complement				1001 1011
	Add 1								        1
	– 100 is represented as					1001 1100

+ 22 in 8–bit two’s–complement binary		0001 0110

– 22 in 8–bit two’s–complement binary
	Represent +22 as an 8–bit number			0001 0110
	Take the one’s complement				1110 1001
	Add 1								        1
	– 22 is represented as					1110 1010

Taking the Two’s Complement (Part 3)

+ 0 in 8–bit two’s–complement binary		0000 0000

– 0 in 8–bit two’s–complement binary
	Represent +0 as an 8–bit number		0000 0000
	Take the one’s complement			1111 1111
	Add 1							        1 Discard the high carry bit
	– 0 is represented as				0000 0000

Claim: – 1 in 8–bit two’s–complement binary is 1111 1111.

– 127 and – 128 in 8–bit two’s–complement binary.

+ 127 in 8–bit two’s–complement binary			0111 1111

– 127 in 8–bit two’s–complement binary
	Represent +127 as an 8–bit number			0111 1111
	Take the one’s complement					1000 0000
	Add 1									        1
	– 127 is represented as						1000 0001

– 128 is “one less” than – 127, so is represented as	1000 0000

Half Adders and Full Adders

A half adder is an adder with no “carry in”.  A full adder is an adder that allows
a “carry in”.  For adding two binary numbers, the “carry in” is either 0 or 1.

In decimal arithmetic on integers,
	a half adder can be used for adding the units column
	a full adder would be used for adding the tens, hundreds, thousands (etc.)
		columns as each of these can have a “carry in” from a column to the right.

The terms “half adder” and “full adder” apply only to binary arithmetic.

A full adder can be converted to a half adder by setting its “carry in” to 0.

Example From Unsigned Integer Arithmetic

Here we add 14 (binary 01110) and 11 (binary 01011) to get 
25 (binary 11001).

Truth Tables for Half Adders and Full Adders

Half-Adder A + B                        	Full-Adder: A + B with Carry In
	A	B	Sum	Carry		A	B	C	Sum	Carry
	0	0	0	0		0	0	0	0	0
	0	1	1	0		0	0	1	1	0
	1	0	1	0		0	1	0	1	0
	1	1	0	1		0	1	1	0	1
						1	0	0	1	0
						1	0	1	0	1
						1	1	0	0	1
						1	1	1	1	1

We don’t really need a full adder to do two’s complement arithmetic, but
	here it is.

Back to algebra.  We were taught that – ( – X) = X for all numbers.
		Let’s test it out for two’s–complement arithmetic.

Double Negations (Part 1)

Remember that the range of 8–bit two’s–complement arithmetic is – 128 to 127.

+ 100 in 8–bit two’s–complement binary		0110 0100

– 100 in 8–bit two’s–complement binary
	Represent +100 as an 8–bit number		0110 0100
	Take the one’s complement				1001 1011
	Add 1								        1
– 100 is represented as						1001 1100

+100 in 8–bit two’s–complement binary
	Represent – 100 as an 8–bit number		1001 1100
	Take the one’s complement				0110 0011
	Add 1								        1
– 100 is represented as						0110 0100

This is the same as + 100.  So – ( – 100) is + 100.

Double Negations (Part 2)

Remember that the range of 8–bit two’s–complement arithmetic is – 128 to 127.

+ 22 in 8–bit two’s–complement binary		0001 0110

– 22 in 8–bit two’s–complement binary
	Represent +22 as an 8–bit number			0001 0110
	Take the one’s complement				1110 1001
	Add 1								        1
– 22 is represented as						1110 1010

+22 in 8–bit two’s–complement binary
	Represent – 22 as an 8–bit number			1110 1010
	Take the one’s complement				0001 0101
	Add 1								        1
+ 22 is represented as						0001 0110

This is the same as + 22.  So – ( – 22) is + 22.

Double Negations (Part 3)

Remember that the range of 8–bit two’s–complement arithmetic is – 128 to 127.

+ 127 in 8–bit two’s–complement binary			0111 1111

– 127 in 8–bit two’s–complement binary
	Represent +127 as an 8–bit number			0111 1111
	Take the one’s complement					1000 0000
	Add 1									        1
– 127 is represented as							1000 0001

– 128 is represented as							1000 0000
		Take the one’s complement				0111 1111
		Add 1								        1
– (– 128) is represented as						1000 0000

– ( – 128) is the same as – 128 !!

What happened?   The answer is that  + 128 cannot be represented in
		8–bit two’s–complement arithmetic.

Standard Ranges

Here is the standard Java implementation of Two’s–Complement arithmetic.

In general the range for N–bit two’s–complement arithmetic is

– 2N–1 to 2N–1 – 1

| Java Type | Number of Bits | Lower Limit | Upper Limit |
| --- | --- | --- | --- |
| byte | 8 | – 128 | 127 |
| short | 16 | – 32768 | 32767 |
| int | 32 | – 2 147 483 648 | 2 147 483 647 |
| long | 64 | – 263 | 263 – 1 |

Log10(2) is about 0.30103.  Log10(3) is about 0.47712.

Log10(263) is about 0.30103 ( 63 = 18.9649.

Log10(9) = Log10(32) = 2(Log10(3) = 2(0.47712 = 0.95424.

As 0.9649 > Log10(9), we conclude that 263 is bigger than 9(1018.

Standard Values in N–Bit Two’s Complement Arithmetic
(With Examples for 16–bit integers)

0	is represented by N zeroes	0000 0000 0000 0000

–1	is represented by N ones	1111 1111 1111 1111

– 2N–1	is represented by a 1 
		followed by (N – 1) zeroes	1000 0000 0000 0000

The student should memorize these patterns and not bother with
	standard conversion techniques when obtaining them.

Technically speaking, the representation of – 2N–1 cannot be derived by
	standard means, as 2N–1 cannot be represented.

Sign Extension

In two’s complement arithmetic, the leftmost bit is the sign bit.

It is		1 for negative numbers
			0 for non–negative numbers

Sign extension is the process of converting a N–bit representation to
	a larger format; e.g., a 16–bit number to a 32–bit number.

Example:

+ 100 in 8–bit two’s–complement binary	0110 0100

+ 100 in 16–bit two’s–complement binary	0000 0000 0110 0100

– 100 in 8–bit two’s–complement binary	1001 1100

– 100 in 16–bit two’s–complement binary	1111 1111 1001 1100

Rule – just extend the sign bit to fill the new “high order” bits.

Overflow: “Busting the Arithmetic”

The range of 16–bit two’s–complement arithmetic is

– 32,768 to 32,767

Consider the following addition problem: 24576 + 24576.
Now + 24,576 (binary 0110 0000 0000 0000) is well within the range.

0110 0000 0000 0000	24576
		0110 0000 0000 0000	24576
		1100 0000 0000 0000	– 16384

What happened?

We had a carry into the sign bit.  This is “overflow”.  The binary representation
		being used cannot handle the result.

NOTE:	This works as unsigned arithmetic.
			24,576 + 24,576 = 49,152 = 32768 + 16384.

When we design a binary adder for N–bit integers (N > 1), we shall address
		the standard method for detecting overflow.

Saturation Arithmetic

Saturation arithmetic is applied to unsigned N–bit integers.

The unsigned range is 0 … 2N – 1.

N = 8	0	through	255
	N = 16	0	through	65535
	N = 32	0	through	4,294,967,295

Saturation arithmetic is commonly applied to 8–bit integers used in
		computer graphics.

RULES:	In addition, if the sum is greater than 2N – 1, set it to 2N – 1.
	In subtraction, if the number is less than 0, set it to 0.

Examples (8–bit saturation arithmetic)

100 + 100		= 200		128 + 128	= 255
	128 + 127		= 255		200 + 200	= 255
								255 + 255	= 255

Result: Brightening a bright scene does not accidentally make it dark.